## Slide 1
Dr. Hassan Ashraf
Assistant Professor_ Civil Engineering Department _ CU Islamabad _ Wah Campus
Internal Rate of Return
EUAW & NPW Method

## Slide 2
Problem # 01
An investment resulted in the following cash flow. Compute the rate of return.
-700
100
175
250
325
0
1
3
2
4

## Slide 3
Problem # 01 EUAW Method
EUAW = EUAB – EUAC = 0 = 100 + 75(A/G,i,4) – 700 (A/P,i,4)
Why we have written this equation?
We have written this equation because internal rate of return is the interest rate at which the present worth and equivalent uniform annual worth are equal to zero.
We will solve the equation by trial and errors. Considering the interest rate as 5% first:
EUAW (5%) = 100 + 75 ( A/G, 5%,4) – 700 (A/P, 5%,4)
= 100 + 75 (1.439) – 700 (0.2820)
= 208 – 197 = +11
The EUAW is too high. If the interest rate is increased, EUAW will decrease. Try i= 8%
EUAW (8%) = 100 + 75 (A/G, 8%,4) – 700 (A/P, 8%, 4)
= 100 + 75 (1.404) – 700 (0.3019)
= 205 – 211 = -6
This time EUAW is too low. We see that the true rate of return is between 5% and 8%. Try I = 7%

## Slide 4
Problem # 01 NPW Method
EUAW (7%) = 100 + 75 (A/G,7%,4) – 700 (A/P,7%,4)
= 100 + 75 (1.416) -700 (0.2952)
= 206 – 206 =0
Therefore, the IRR is 7%.
We can solve this problem using Net Present Worth also.
Starting the interest rate at i= 4%
NPW = -700 + 100 (P/A,4%,4) + 75 ( P/G,4%,4)
= -700 + (3.630) + 75 ( 5.267)
= -700 + 363 + 395.025
= 58.025
NPW = -700 + 100 (P/A, 6%, 4) + 75 ( P/G, 6%,4)
= -700 + 100 ( 3.465) + 75 (4.945)
= -700 + 346.5 + 370.875
= 17.375

## Slide 5
Problem # 01
= -700 + 100 ( 3.387) + 75 (4.795) on 7%
= -700 +338.7 + 359.625
= -1.675
X | X1 | X2
X | 6% | 7%
0 | 17.375 | -1.675
Y | Y1 | Y2
Y= y1 + [(x-x1)/(x2-x1)] (y2-y1)
= 17.375 + ( x – 0.06) ( -1905)
= 17.375 – 1905x + 114.3
1905x = 131.675
x = 131.675/1905 = 6.912%

## Slide 6
Problem # 02
A new corporate bond was initially sold by a stockbroker to an investor for $1000. The issuing corporation promised to pay the bondholder $40 interest on the $1000 face value of the bond every 6 months, and to repay the $1000 at the end of 10 years. After one year the bond was sold by the original buyer for $950.
(a) What rate of return did the original buyer receive on his investment?
(b) What rate of return can the new buyer (paying $950) expect to receive if he keeps the bond for its remaining 9-year life?
Lets solve the problem using EUAW.
EUAW = EUAB – EUAC = 40 + 950 ( P/F, i%,2) (A/P, i%,2) – 1000 ( A/P,i%,2)
Lets start with 2%
= 40 + 950 (.9612)(0.5151) – 1000 (0.5151)
= 40 + 470.358 – 515.1 = -4.742

## Slide 7
Problem # 02
Lets try 1.5%
EUAW = EUAB – EUAC = 40 + 950 ( P/F, i%,2) (A/P, i%,2) – 1000 ( A/P,i%,2)
Lets start wit%
= 40 + 950 (.9707)(0.5113) – 1000 (0.5113)
= 40 + 470.358 – 511.3 = 0.2 which nearly equal to zero .
The interest rate calculated is per 6 months basis. In order to calculate the nominal interest rate ( annual basis ) = 1.5% x 2 = 3%
As the compounding was on semi-annual basis, we must find effective interest rate. Therefore,
i-eff = ( 1+ r/M)^M -1
= ( 1 + 0.03/2)^2 -1 = 3.022%

## Slide 8
Problem # 2
950
40
40
0
40
40
40
40
40
40
40
40
40
1000
Lets try 5%
EUAW = EUAB – EUAC = 40 + 1000 ( P/F, i%,18) (A/P, i%,18) – 950 ( A/P,i%,18)
= 40 + 1000 (.4155)(.0855) – 950 (0.0855)
= 40 + 35.52 – 81.225 = -5.705
Now Lets try 4%
EUAW = EUAB –EUAC = 40 +1000 (P/F,i%,18) (A/P,i%,18) – 950 (A/P,i%,18)

## Slide 9
Internal Rate of Return
EUAW = EUAB –EUAC = 40 +1000 (P/F,i%,18) (A/P,i%,18) – 950 (A/P,i%,18)
= 40 + 1000 (.4936) (.0790) – 950 (.0790)
= 40 + 38.9944- 75.05
= 3.944
So, no we have no option but to interpolate between the interest values of 4% and 5%
X | X1 | X2
X | 4% | 5%
0 | 3.944 | -5.705
Y | Y1 | Y2

## Slide 10
Internal Rate of Return
X | X1 | X2
X | 4% | 5%
0 | 3.944 | -5.705
Y | Y1 | Y2
Y= y1 + [(x-x1)/(x2-x1)] (y2-y1)
= 3.944 + ( x – 0.04) ( -964.9)
= 3.944 – 964.9x + 38.59
964.9x = 42.534
x = 42.534/964.9 = 4.41%
This interest period has been calculated on 6 month basis.
So the nominal interest rate on annual basis is 4.41x2 = 8.82%
i-eff = ( 1+ 0.0441)^2 – 1 = 9.014%

## Slide 11
Thank You