## Slide 1
Dr. Hassan Ashraf
Assistant Professor_ Civil Engineering Department _ CU Islamabad _ Wah Campus
Internal Rate of Return
Incremental Analysis

## Slide 2
Problem # 01
When there are two alternatives, rate of return analysis is performed by computing the incremental rate of return on the difference between the alternatives.
If an electromagnet is installed on the input conveyor of a coal-processing plant, it will pick up scrap metal in the coal. Removing this scrap will save an estimated $1200 per year in costs associated with machinery damage. The electromagnetic equipment has an estimated useful life of 5 years and no salvage value. Two suppliers have been contacted: Leaseco will provide the equipment in return for three beginning-of-year annual payments of $1000 each; Saleco will provide the equipment for $2783. If the MARR is 10%, should the project be done, and if so, which supplier should be selected?
What we need to do is to tabulate cash flows for both alternatives and then apply NPW on the difference between the the cashlow values of saleco and Leaseco.

## Slide 3
Problem # 01
Year | Leaseco | Saleco | Saleco-Leaseco
0 | -1000 | -2783 | -1783
1 | -1000 1200 | 1200 | 1000
2 | -1000 1200 | 1200 | 1000
3 | 1200 | 1200 | 0
4 | 1200 | 1200 | 0
5 | 1200 | 1200 | 0
NPW = -1783 + 1000 ( P/A, i%,2) …………………. Let try 8%
= -1783 + 1000 (1.783) = -1783 + 1783 =0
Therefore, it means IRR for the cashflow between the alternatives is 8%. However, this is less than the 10% MARR. Therefore, we will select Leaseco instead of Saleco.

## Slide 4
Problem # 02
Select one alternative between the two mutually exclusive alternatives.
Year | Alt.1 | Alt.2 | Alt2 – Alt 1
0 | -$1000 | -2000 | 1000
1 | +$1500 | +$2800 | 1300
NPW = -1000 + 1300 ( P/F, i%,1) …………………. Let try 30%
= -1000 + 1300 (.7692) = -1000 + 1000 =0
Therefore, it means IRR for the cash flow between the alternatives is 3%. It further indicates that the 30% rate of return on the difference between the alternatives is far higher than the 6% MARR. The additional $1000 investment to obtain Alt.2 is superior to investing the $1000 else at 6%. To obtain this desirable increment of investment, with its 30% rate o return, Alt. 2 is selected.

## Slide 5
Problem # 03
A ﬁrm is considering which of two devices to install to reduce costs. Both devices have useful lives of 5 years and no salvage value. Device A costs $1000 and can be expected to result in $300 savings annually. Device B costs $1350 and will provide cost savings of $300 the ﬁrst year but will increase $50 annually, making the second-year savings $350, the third-year savings $700, and so forth. For a 7% MARR, which device should the ﬁrm purchase?
Year | Device A | Device B | Device B- Device A
0 | -1000 | -1350 | -350
1 | 300 | 300 | 0
2 | 300 | 350 | 50
3 | 300 | 400 | 100
4 | 300 | 450 | 150
5 | 300 | 500 | 200

## Slide 6
Problem # 03
The NPW Eq. for the cash flow representing the difference between the two alternatives is as under:
NPW = -350 + 50 (P/A,i%,4) (P/F, i%,1)+50(P/G,i%,4) (P/F, i%, 1)
Lets try 8%
= -350 + 50 (3.312) (0.9259) + 50 (4.65) (0.9259)
= -350 + 153.32 + 215.27 =18.59
Now Lets try 10%
= -350 + 50 ( 3.17 ) (.9091) + 50 ( 4.378 ) (.9091)
= -350 + 144.09 + 199
= -6.91

## Slide 7
Problem # 03
X | X1 | X2
X | 8% | 10%
0 | 18.59 | -6.91
Y | Y1 | Y2
Y= y1 + [(x-x1)/(x2-x1)] (y2-y1)
= 18.59 + (x-.08) (-1275)
= 18.59 -1275x + 102
x = 120.59/1275 = 0.0945 = 9.45%
The 9.45% IRR is greater than 7% MARR; therefore, the increment is desirable. Reject Device A and Choose Device B.

## Slide 8
Problem # 04
Two Machines are being considered for purchase. If the MARR is 10%, which machine should be bought? Use an IRR analysis comparison.
 | Machine X | Machine Y
Initial Cost | 200 | 700
Uniform Annual Benefit | 95 | 120
End-of-useful-life salvage value | 50 | 150
Useful life, in years | 6 | 12

## Slide 9
Problem # 04
 | Machine X | Machine Y | Machine Y – Machine X
0 | -200 | -700 | -500
1 | 95 | 120 | 25
2 | 95 | 120 | 25
3 | 95 | 120 | 25
4 | 95 | 120 | 25
5 | 95 | 120 | 25
6 | 95 50 -200 | 120 | 25 150
7 | 95 | 120 | 25
8 | 95 | 120 | 25
9 | 95 | 120 | 25
10 | 95 | 120 | 25
11 | 95 | 120 | 25
12 | 95 50 | 120 150 | 100

## Slide 10
Problem # 04
PW of Cost (differences) = PW of benefits ( differences)
500 = 25 ( P/A ,i, 12) + 150 (P/F,i,6)+100 (P/F,i,12)
The sum of benefits over the 12 years is $550, which is only a little greater than the $500 additional cost. This indicates that the rate of return is quite low. Try i = 1%
500 = 25 ( 11.255) + 150 (0.942) + 100 ( 0.887)
= 281 + 141 +89 = 511
The interest rate is too low, Try i=1.5%
500 = 25 (10.908) + 150 (0.914) + 100 (0.836)
= 273 + 137 + 184 = 494

## Slide 11
Problem # 04
X | X1 | X2
X | 1% | 1.5%
0 | 11 | -6
Y | Y1 | Y2
Y= y1 + [(x-x1)/(x2-x1)] (y2-y1)
= 11 + (x-.01)(-3400)
= 11 -3400x + 34
X = 45/3400 = .0132 = 1.32%
The Machine Y-X increment IRR is about 1.32%, far below the 10% MARR. The additional investment to obtain Machine Y yields an unsatisfactory rate of return, therefore X is the preferred alternative.

## Slide 12
Thank You